## Slide 1: Network+ Guide to Networks 7th Edition
Chapter 4
Structured Cabling and Networking Elements
Notes: Network+ Guide to Networks 7th Edition
Chapter 4
Structured Cabling and Networking Elements

## Slide 2: Objectives
Identify the best practices for managing networks and cabling equipment in commercial buildings and work areas
Explain issues related to managing power and the environment in which networking equipment operates
Describe characteristics of NIC and Ethernet interfaces
Troubleshoot network devices and create a network map to be used for network troubleshooting
Notes: Objectives
Identify the best practices for managing networks and cabling equipment in commercial buildings and work areas
Explain issues related to managing power and the environment in which networking equipment operates
Describe characteristics of NIC and Ethernet interfaces
Troubleshoot network devices and create a network map to be used for network troubleshooting

## Slide 3: Network Equipment in Commercial Buildings
TIA/EIA’s joint 568 Commercial Building Wiring Standard
  Also known as structured cabling
  Describes the best way to install networking media to maximize performance and minimize upkeep
  Apply no matter what type of media, transmission technology, or networking speeds are involved
  Based on hierarchical design and assumes a network is based on the start topology
Notes: Network Equipment in Commercial Buildings
TIA/EIA’s joint 568 Commercial Building Wiring Standard
  Also known as structured cabling
  Describes the best way to install networking media to maximize performance and minimize upkeep
  Apply no matter what type of media, transmission technology, or networking speeds are involved
  Based on hierarchical design and assumes a network is based on the start topology

## Slide 4: Network Equipment in Commercial Buildings
Notes: Network Equipment in Commercial Buildings

## Slide 5: Network Equipment in Commercial Buildings
Components
  Entrance facilities
  MDF (main distribution frame)
  IDF (intermediate distribution frame)
  Horizontal wiring
  Backbone wiring
  Work area
Notes: Network Equipment in Commercial Buildings
Components
  Entrance facilities
  MDF (main distribution frame)
  IDF (intermediate distribution frame)
  Horizontal wiring
  Backbone wiring
  Work area

## Slide 6: Network Equipment in Commercial Buildings
Notes: Network Equipment in Commercial Buildings

## Slide 7: Network Equipment in Commercial Buildings
Notes: Network Equipment in Commercial Buildings

## Slide 8: Network Equipment in Commercial Buildings
Notes: Network Equipment in Commercial Buildings

## Slide 9: Cable Management
Cable installation tips to prevent Physical layer failures:
  When terminating twisted-pair cabling, don’t leave more than 1 inch of exposed cable before a termination
  Do not exceed the cable’s prescribed bend radius (radius of the maximum arc into which you can loop a cable without impairing data transmission)
  Use a cable tester to verify that each cable segment transmits data reliably
  Cinch cables loosely
Notes: Cable Management
Cable installation tips to prevent Physical layer failures:
  When terminating twisted-pair cabling, don’t leave more than 1 inch of exposed cable before a termination
  Do not exceed the cable’s prescribed bend radius (radius of the maximum arc into which you can loop a cable without impairing data transmission)
  Use a cable tester to verify that each cable segment transmits data reliably
  Cinch cables loosely

## Slide 10: Cable Management
Cable installation tips (cont’d):
  Avoid laying cables across a floor and use cord covers if they must be exposed
  Avoid EMI
  Make sure cable sheath is plenum-rated
  Pay attention to grounding requirements
  Leave some slack in cable runs
  Use cable management devices such as cable trays, braided sleeving, and furniture grommets
  Use patch panels to organize and connect lines
Notes: Cable Management
Cable installation tips (cont’d):
  Avoid laying cables across a floor and use cord covers if they must be exposed
  Avoid EMI
  Make sure cable sheath is plenum-rated
  Pay attention to grounding requirements
  Leave some slack in cable runs
  Use cable management devices such as cable trays, braided sleeving, and furniture grommets
  Use patch panels to organize and connect lines

## Slide 11: Cable Management
Cable installation tips (cont’d):
  You or your network manager should specify standards for the types of cable used by your organization
  Keep your cable plant documentation accessible
  Label every data jack or port, patch panel and connector
  Use color-coded cables for different purposes
  Update your documentation as you make changes to the network
Notes: Cable Management
Cable installation tips (cont’d):
  You or your network manager should specify standards for the types of cable used by your organization
  Keep your cable plant documentation accessible
  Label every data jack or port, patch panel and connector
  Use color-coded cables for different purposes
  Update your documentation as you make changes to the network

## Slide 12: Device Management
Maintaining up-to-date records about your network devices will reduce your workload
  Will also make troubleshooting easier and more efficient
In order to keep track of devices
  Name them systematically and label them
Notes: Device Management
Maintaining up-to-date records about your network devices will reduce your workload
  Will also make troubleshooting easier and more efficient
In order to keep track of devices
  Name them systematically and label them

## Slide 13: Labeling and Naming Conventions
Tips for labeling:
  Use color-coded cables for different purposes and use cable tags to identify each cable’s purpose
  Label the ports and jacks that cables connect to
  Use a portable label maker and use labels that are durable and are designed to stick to plastic and metal
  Where labels won’t fit on the device, draw a simple diagram of each device that indicates how each port is used
  Use names that are as descriptive as possible
  Use established naming conventions
Notes: Labeling and Naming Conventions
Tips for labeling:
  Use color-coded cables for different purposes and use cable tags to identify each cable’s purpose
  Label the ports and jacks that cables connect to
  Use a portable label maker and use labels that are durable and are designed to stick to plastic and metal
  Where labels won’t fit on the device, draw a simple diagram of each device that indicates how each port is used
  Use names that are as descriptive as possible
  Use established naming conventions

## Slide 14: Labeling and Naming Conventions
Notes: Labeling and Naming Conventions

## Slide 15: Rack Systems
Rack systems - provide mounting hardware for network equipment to optimize the use of square footage in equipment rooms
  And ensure adequate spacing, access, and ventilation for these devices
  Come in a standard 19-inch frame, but may also come across a 23-inch rack that includes the entire width of the rack
  Racks may be wall- or ceiling-mounted, or freestanding on the floor
  Racks are measured in rack units (RU or U)
Notes: Rack Systems
Rack systems - provide mounting hardware for network equipment to optimize the use of square footage in equipment rooms
  And ensure adequate spacing, access, and ventilation for these devices
  Come in a standard 19-inch frame, but may also come across a 23-inch rack that includes the entire width of the rack
  Racks may be wall- or ceiling-mounted, or freestanding on the floor
  Racks are measured in rack units (RU or U)

## Slide 16: Rack Systems
Figure 4-13 Two-post and four-post racks
Notes: Rack Systems

## Slide 17: Rack Systems
In a typical rack system, airflow through the chassis is typically designed to move from front to back
  Rack-monitoring systems should be installed to sound an alarm if the overall temperature rises too much
Notes: Rack Systems
In a typical rack system, airflow through the chassis is typically designed to move from front to back
  Rack-monitoring systems should be installed to sound an alarm if the overall temperature rises too much

## Slide 18: NAS (Network Attached Storage)
Fault tolerance - techniques that allow data storage or other operations to continue in the event of a failure or fault of one its components
NAS - a specialized storage device or group of storage devices that provides centralized fault tolerant data storage for a network
  Contains its own file system optimized for saving and serving files
  Reads and writes from its disk significantly faster than other types of servers
  Can be easily expanded without interrupting service
Notes: NAS (Network Attached Storage)
Fault tolerance - techniques that allow data storage or other operations to continue in the event of a failure or fault of one its components
NAS - a specialized storage device or group of storage devices that provides centralized fault tolerant data storage for a network
  Contains its own file system optimized for saving and serving files
  Reads and writes from its disk significantly faster than other types of servers
  Can be easily expanded without interrupting service

## Slide 19: NAS (Network Attached Storage)
A NAS device cannot communicate directly with clients
  Clients go through a file server, which communicates with the NAS device
Notes: NAS (Network Attached Storage)
A NAS device cannot communicate directly with clients
  Clients go through a file server, which communicates with the NAS device

## Slide 20: SANs (Storage Area Networks)
A SAN is a network of storage devices that communicate directly with each other and with other networks
  Uses a type of architecture that is similar to mesh topology, which is very fault-tolerant
SANS use one of two types of Transport layer protocols:
  Fibre Channel (FC)
  iSCSI
Notes: SANs (Storage Area Networks)
A SAN is a network of storage devices that communicate directly with each other and with other networks
  Uses a type of architecture that is similar to mesh topology, which is very fault-tolerant
SANS use one of two types of Transport layer protocols:
  Fibre Channel (FC)
  iSCSI

## Slide 21: SANs (Storage Area Networks)
Notes: SANs (Storage Area Networks)

## Slide 22: SANs (Storage Area Networks)
A SAN can be installed in a location separate from the LAN it serves
SANs are highly scalable and have:
  A very high fault tolerance
  Massive storage capabilities
  Fast data access
SANs are best suited to environments with huge quantities of data that must always be quickly available
Notes: SANs (Storage Area Networks)
A SAN can be installed in a location separate from the LAN it serves
SANs are highly scalable and have:
  A very high fault tolerance
  Massive storage capabilities
  Fast data access
SANs are best suited to environments with huge quantities of data that must always be quickly available

## Slide 23: Managing Power Sources and the Environment
Part of managing a network is managing power sources to account for outages and fluctuations
You also need to monitor and manage the environment that might affect sensitive network equipment
Notes: Managing Power Sources and the Environment
Part of managing a network is managing power sources to account for outages and fluctuations
You also need to monitor and manage the environment that might affect sensitive network equipment

## Slide 24: Power Management
Power surges can cause serious damage to sensitive computer equipment
  Can be a frustrating source of network problems
Arm yourself with an understanding of:
  The nature of an electric circuit
  Electrical components that manage electricity
Notes: Power Management
Power surges can cause serious damage to sensitive computer equipment
  Can be a frustrating source of network problems
Arm yourself with an understanding of:
  The nature of an electric circuit
  Electrical components that manage electricity

## Slide 25: Power Flaws
Power flaws that can damage your equipment:
  Surge - momentary increase in voltage due to lightning strikes, solar flares, or electrical problems
  Noise - fluctuation in voltage levels caused by other devices on the network or EMI
  Brownout - momentary decrease in voltage; also known as a sag
  Blackout - complete power loss
Notes: Power Flaws
Power flaws that can damage your equipment:
  Surge - momentary increase in voltage due to lightning strikes, solar flares, or electrical problems
  Noise - fluctuation in voltage levels caused by other devices on the network or EMI
  Brownout - momentary decrease in voltage; also known as a sag
  Blackout - complete power loss

## Slide 26: UPS (Uninterruptible Power Supply)
UPS - a battery-operated power source directly attached to devices and to a power supply
  Prevents undesired fluctuations of power from harming the device or interrupting its services
Two UPS categories:
  Standby UPS - provides continuous voltage to a device by switching to the battery when it detects a loss of power from the wall outlet
  Online UPS - uses the AC power from the wall outlet to continuously charge its battery, while providing power to the device through its battery
Notes: UPS (Uninterruptible Power Supply)
UPS - a battery-operated power source directly attached to devices and to a power supply
  Prevents undesired fluctuations of power from harming the device or interrupting its services
Two UPS categories:
  Standby UPS - provides continuous voltage to a device by switching to the battery when it detects a loss of power from the wall outlet
  Online UPS - uses the AC power from the wall outlet to continuously charge its battery, while providing power to the device through its battery

## Slide 27: UPS (Uninterruptible Power Supply)
To decide which UPS is right for your network, consider the following:
  Amount of power needed
  Period of time to keep a device running
  Line conditioning
  Cost
Testing UPSs with your equipment is an important part of the decision-making process
  Some manufacturers will let you test the UPS
Notes: UPS (Uninterruptible Power Supply)
To decide which UPS is right for your network, consider the following:
  Amount of power needed
  Period of time to keep a device running
  Line conditioning
  Cost
Testing UPSs with your equipment is an important part of the decision-making process
  Some manufacturers will let you test the UPS

## Slide 28: Generators
Generator - backup power source, providing power redundancy in the event of a total blackout
  Can be powered by diesel, liquid propane gas, natural gas, or steam
Generators can be combined with large UPSs to ensure that clean power is always available
If an organization relies on a generator, fuel levels and quality should be checked regularly
Notes: Generators
Generator - backup power source, providing power redundancy in the event of a total blackout
  Can be powered by diesel, liquid propane gas, natural gas, or steam
Generators can be combined with large UPSs to ensure that clean power is always available
If an organization relies on a generator, fuel levels and quality should be checked regularly

## Slide 29: Generators
Notes: Generators

## Slide 30: Monitoring the Environment and Security
Data rooms are often service by HVAC systems separate from the rest of the building
Specialized products can monitor the critical factors of a data closet’s environment:
  Unacceptable temperature
  Humidity
  Airflow conditions
Every data room should be locked with only limited IT personnel having keys
  Security cameras are suggested
Notes: Monitoring the Environment and Security
Data rooms are often service by HVAC systems separate from the rest of the building
Specialized products can monitor the critical factors of a data closet’s environment:
  Unacceptable temperature
  Humidity
  Airflow conditions
Every data room should be locked with only limited IT personnel having keys
  Security cameras are suggested

## Slide 31: NICs and Ethernet
Each workstation, server, printer, connectivity device, or other device on a network uses a NIC
On local networks, a NIC uses Ethernet standards for communication
Notes: NICs and Ethernet
Each workstation, server, printer, connectivity device, or other device on a network uses a NIC
On local networks, a NIC uses Ethernet standards for communication

## Slide 32: Characteristics of NICs
The NIC contains a transceiver that transmits and receives data signals over network media
NICs belong to both the Physical and Data Link layer because they:
  Issue data signals and assemble/disassemble data frames
  Interpret physical addressing information
  Perform routines that determine which node has the right to transmit data
  Can also perform prioritization, network management, buffering, and traffic-filtering functions
Notes: Characteristics of NICs
The NIC contains a transceiver that transmits and receives data signals over network media
NICs belong to both the Physical and Data Link layer because they:
  Issue data signals and assemble/disassemble data frames
  Interpret physical addressing information
  Perform routines that determine which node has the right to transmit data
  Can also perform prioritization, network management, buffering, and traffic-filtering functions

## Slide 33: Characteristics of NICs
NICs come in a variety of types depending on:
  Connection type
  Maximum network transmission speed
  Connector interfaces
  Number of connector interfaces, or ports
  Manufacturer
  Support for enhanced features, such as PoE+, buffering, or traffic management
  Method of interfacing with the computer’s motherboard and interface standards
Notes: Characteristics of NICs
NICs come in a variety of types depending on:
  Connection type
  Maximum network transmission speed
  Connector interfaces
  Number of connector interfaces, or ports
  Manufacturer
  Support for enhanced features, such as PoE+, buffering, or traffic management
  Method of interfacing with the computer’s motherboard and interface standards

## Slide 34: Characteristics of NICs
A NIC interfaces with a computer’s motherboard by one of the following methods:
  Integrated into the motherboard
  Installed in an expansion slot on the motherboard
  Installed as a peripheral device
Notes: Characteristics of NICs
A NIC interfaces with a computer’s motherboard by one of the following methods:
  Integrated into the motherboard
  Installed in an expansion slot on the motherboard
  Installed as a peripheral device

## Slide 35: Characteristics of NICs
Notes: Characteristics of NICs

## Slide 36: Characteristics of NICs
General tips when installing NICs:
  Install hardware and software
  Install a peripheral NIC
  Install an expansion card NIC
  Install multiple NICs in servers and other high-powered computers
Notes: Characteristics of NICs
General tips when installing NICs:
  Install hardware and software
  Install a peripheral NIC
  Install an expansion card NIC
  Install multiple NICs in servers and other high-powered computers

## Slide 37: Simplex, Half-Duplex, and Duplex
Methods of transmission:
  Full-duplex, also called duplex - signals are free to travel in both directions over a medium simultaneously
  Half-duplex - signals may travel in both directions over a medium but in only one direction at a time
  Simplex - signals may travel in only one direction
    Sometimes called one-way or unidirectional
Many network devices allow you to specify whether the device should use half- or full-duplex
  Modern NICs use full-duplex by default
Notes: Simplex, Half-Duplex, and Duplex
Methods of transmission:
  Full-duplex, also called duplex - signals are free to travel in both directions over a medium simultaneously
  Half-duplex - signals may travel in both directions over a medium but in only one direction at a time
  Simplex - signals may travel in only one direction
    Sometimes called one-way or unidirectional
Many network devices allow you to specify whether the device should use half- or full-duplex
  Modern NICs use full-duplex by default

## Slide 38: Simplex, Half-Duplex, and Duplex
Auto Negotiation - allows the NIC to select the best link speed and duplex that is also supported by the neighboring device
If you specify a particular speed and duplex that is not supported by a neighboring device
  The result is a speed and duplex mismatch and transmission will fail
Using UNIX or Linux, the ethtool utility allows you to view and change NIC settings
Notes: Simplex, Half-Duplex, and Duplex
Auto Negotiation - allows the NIC to select the best link speed and duplex that is also supported by the neighboring device
If you specify a particular speed and duplex that is not supported by a neighboring device
  The result is a speed and duplex mismatch and transmission will fail
Using UNIX or Linux, the ethtool utility allows you to view and change NIC settings

## Slide 39: Ethernet Frames
Ethernet is a Layer 2 standard that:
  Is flexible
  Capable of running on a variety of network media
  Offers excellent throughput at a reasonable cost
Ethernet II is the current Ethernet standard
Notes: Ethernet Frames
Ethernet is a Layer 2 standard that:
  Is flexible
  Capable of running on a variety of network media
  Offers excellent throughput at a reasonable cost
Ethernet II is the current Ethernet standard

## Slide 40: Ethernet Frames

## Slide 41: Troubleshooting Network Devices
This section takes a look at some approaches to troubleshooting NIC problems
  Apply what you have learned so far by completing Applying Concepts activities in this section
Notes: Troubleshooting Network Devices
This section takes a look at some approaches to troubleshooting NIC problems
  Apply what you have learned so far by completing Applying Concepts activities in this section

## Slide 42: Building and Maintaining Network Documentation
Having up-to-date and detailed documentation of your network is essential to good troubleshooting
Network diagrams - graphical representations of a network’s devices and connections
  May show physical layout, logical topology, IP address reserves, names of major network devices, and types of transmission media
Network mapping - the process of discovering and identifying the devices on a network
Notes: Building and Maintaining Network Documentation
Having up-to-date and detailed documentation of your network is essential to good troubleshooting
Network diagrams - graphical representations of a network’s devices and connections
  May show physical layout, logical topology, IP address reserves, names of major network devices, and types of transmission media
Network mapping - the process of discovering and identifying the devices on a network

## Slide 43: Building and Maintaining Network Documentation
To adequately manage a network, record the following:
  Network diagrams
  Physical topology
  Access methods
  Protocols
  Devices
  Operating systems
  Applications
  Configurations
Notes: Building and Maintaining Network Documentation
To adequately manage a network, record the following:
  Network diagrams
  Physical topology
  Access methods
  Protocols
  Devices
  Operating systems
  Applications
  Configurations

## Slide 44: Building and Maintaining Network Documentation
Notes: Building and Maintaining Network Documentation

## Slide 45: Building and Maintaining Network Documentation
Network diagrams provide broad snapshots of a network’s physical or logical topology
  Useful for planning where to insert a new switch or determining how a particular router, gateway, or firewall interact
Wiring schematic - a graphical representation of a network’s wired infrastructure
  In detailed form, it shows every wire necessary to interconnect network devices
Notes: Building and Maintaining Network Documentation
Network diagrams provide broad snapshots of a network’s physical or logical topology
  Useful for planning where to insert a new switch or determining how a particular router, gateway, or firewall interact
Wiring schematic - a graphical representation of a network’s wired infrastructure
  In detailed form, it shows every wire necessary to interconnect network devices

## Slide 46: Building and Maintaining Network Documentation
Notes: Building and Maintaining Network Documentation

## Slide 47: Summary
TIA/EIA created a joint cabling standard known as structured cabling
Physical layer failures can be caused by a range of issues, including poor termination, excessive bend radius, damaged cables, and EMI
Rack systems provide mounting hardware for network equipment to optimize the use of square footage in equipment rooms
NAS (network attached storage) provides centralized fault-tolerant data storage for a network
Notes: Summary
TIA/EIA created a joint cabling standard known as structured cabling
Physical layer failures can be caused by a range of issues, including poor termination, excessive bend radius, damaged cables, and EMI
Rack systems provide mounting hardware for network equipment to optimize the use of square footage in equipment rooms
NAS (network attached storage) provides centralized fault-tolerant data storage for a network

## Slide 48: Summary
SAN is a network of multiple storage devices that collectively provide faster access to data and larger amounts of storage than a NAS can do
Fibre Channel connects devices within a SAN
iSCSI runs on top of TCP on an already established Ethernet LAN
A UPS is a battery-operated power source directly attached to one or more devices and a power supply
Standard generators do not provide surge protection but can provide a backup power source
Notes: Summary
SAN is a network of multiple storage devices that collectively provide faster access to data and larger amounts of storage than a NAS can do
Fibre Channel connects devices within a SAN
iSCSI runs on top of TCP on an already established Ethernet LAN
A UPS is a battery-operated power source directly attached to one or more devices and a power supply
Standard generators do not provide surge protection but can provide a backup power source

## Slide 49: Summary
NICs interpret physical addressing information to ensure data is delivered to its proper destination
On a Linux workstation, a popular utility called ethtool allows you to view and change NIC settings
Ethernet is a Layer 2 standard that is a flexible technology, capable of running on a variety of media
An Ethernet II frame can range in size from 64 to 1522 total bytes
Notes: Summary
NICs interpret physical addressing information to ensure data is delivered to its proper destination
On a Linux workstation, a popular utility called ethtool allows you to view and change NIC settings
Ethernet is a Layer 2 standard that is a flexible technology, capable of running on a variety of media
An Ethernet II frame can range in size from 64 to 1522 total bytes

## Slide 50: Summary
To troubleshoot NIC problems, use a loopback plug, Device Manager in Windows, or ethtool in Linux or UNIX, NIC diagnostics software, and command-line utilities
Network maps may show physical layout, logical topology, IP address reserves, names of major network devices, and types of transmission media
Several programs are available to assist in detecting, identifying, and monitoring the devices on your network
Notes: Summary
To troubleshoot NIC problems, use a loopback plug, Device Manager in Windows, or ethtool in Linux or UNIX, NIC diagnostics software, and command-line utilities
Network maps may show physical layout, logical topology, IP address reserves, names of major network devices, and types of transmission media
Several programs are available to assist in detecting, identifying, and monitoring the devices on your network